## Slide 1
Yogesh Prem Swami
SGX Remote Attestation is not sufficient

## Slide 2: HW/SW crypto co-design
Software Simulation of HW as attack vector
Class-1 Simulation
  Simulate HW on any UTM
  Counter measure: Oracle access to a hardware resident key
Cass-2 Simulation
  Run simulator inside real hardware
  Simulator gets (oracle) access to keys
  Counter measure: More difficult
SGX is secure against both!
Class-1 Simulator
enclave
SGX
enclave
SGX Simulator
attacker
Class-2 Simulator
enclave
SGX
enclave
SGX Simulator
attacker
SGX

## Slide 3: Common SGX Enclave Design
STEP-1: Define a generic Remote Attestation Scheme
STEP-2: Arbitrarily compose different cryptographic schemes
  Load encrypted Private Key from Disk into Enclave
  Load authenticated Public Keys from Disk into Enclave
  Create signed/mac-ed Audit Log of events (e.g., which key was used, etc.)
  Make arbitrary ecalls, ocalls, and exit from enclave due to interrupts
STEP-3: Define a workflow that combines STEP-1 and STEP-2 to achieve the goal
Several examples (both published as well as propriety)
Is this design paradigm secure?

## Slide 4: Sequential Composition
Example vacuously broken
  Attacker runs attestation correctly
  Runs rest of the protocol outside the enclave
Enclave is a single protocol sequentially composed of sub-protocols
  Not unconditionally secure
  Numerous examples
    Log commitments etc. can be devastating
If |1| > 2x and the |2| > 2y then
  1 2 ≠ 2 1
  |i j | ≱ 2min{x,y}

## Slide 5: Concurrent Composition
Attacker runs the same enclave concurrently
  Feed the same <tpm_cntr,tpm_sig> to both instances
Concurrent composition not limited to running same operation
SGX Has no in-built replay protection
  Adding TPM to TCB non-trivial
  TPM and CPU needs mutual auth (motherboard/CPU swap!)
Launch Enclave cannot limit concurrency
  EINITTOKEN is a long-term credential
  Whitelist ineffective

## Slide 6: SGX Computational Model
SGX enclave is not a black-box (Oracle)
  Adversary can force the enclave to exit at arbitrary execution point via AEX
  SGX allows making ecalls after returning from interrupts
SGX allows multiple threads within the same enclave
  Select number of allowed threads carefully!
Makes global state in enclave malleable
Requires careful ecall interface for Proof-of-Knowledge (PoK) protocols

## Slide 7: State Malleability and PoK extractor
static int auth_count = 0; struct general_info{ char general_name[256]; const sgx_ec256_public_t general_pub; bool has_authorized; // initialized to false }GENERALS[] = { … };
int auth_and_launch(const char* const general_name, const sgx_ec256_signature_t* sig) { struct general_info* valid_general = validate_general(general_name, sig);
if(!valid_general){ return INVALID_GENERAL; }
if(!valid_general->has_authorized){ auth_count++; // AEX here will be devastating! valid_general->has_authorized = true; }else{ return GENERAL_ALREADY_AUTHORIZED_ACTION; }
if(auth_count == 2){ … } … }
Attacker artificially creates AEX at desired location
  Run the same enclave in parallel for poly(instr-count) times
  Interrupt processor randomly
Make ecall with same input parameter
With multiple threads, one might be able to exploit PoK protocols

## Slide 8: SGX Remote Attestation Big Picture
EPID Blinded Join and
PoK of RoT
SGX Hardware contains a 128-bit secret that’s known to Intel
  Interpretation/use of this secret left to software
  Access controlled by Launch Enclave
Used as Root-of-Trust between Intel Attestation Service (IAS) and the CPU
  Proof-of-Knowledge of this secret deciding factor on who gets to join EPID SGX Group
Remote Attestation based on EPID Group Signatures
SGX Processor
IAS
RoT established at mfg
EPID Key Gen
Group Credentials (if PoK valid)
Gen Quote

## Slide 9: SGX Key Hierarchy
Two statistically independent base keys
Root Provisioning Key
  Known to Intel
  Used during EPID Join
Root Seal Key
  Intel claims not to know this
  Unclear if key is generation via oracle access or injected from outside
Several named-keys derived from base key
  Coarse Access Control by Launch Enclave

## Slide 10: SGX Key Derivation
Each named key can further be diversified
  Enclave’s own identity (mrenclave, mrsigner, attributes)
  Potentially adversarially selected 128-bit random number
Identity used directly from CPU’s private data structures
  Absence  Use zeros
Keys cannot be diversified for other enclave’s identity

## Slide 11: Group Signature Overview
Sign messages on behalf of the group
  Single group public-key
  Unique member private-key
  Group manager decides who can join
Fully Anonymity [BMW03]:
  Adversary cannot tell which member signed the message even if it has private-key of each member
Full Traceability [BSZ04]:
  A privileged entity (Opener) can find out who signed the message
Non-Frameability [BSZ04]:
  A sub-set  of group members cannot create a valid signature which the opener attributes to someone outside of 

## Slide 12: Enhanced Privacy ID (EPID)
Based on BBS+ scheme [BBS03, ASM06]
Almost standard construction
  Join: BBS+ signature on member’s private-key in zero-knowledge
  Sign: Proves knowledge of BBS+ signature of group manager on private-key in zero-knowledge
Blinded join process
  Group manager never knows the member’s private key
  No concurrent join by default

## Slide 13: EPID Revocation
Private-Key Base Revocation (Priv-RL)
  Member’s private-key directly placed in the revocation list
  Retroactively destroys member’s privacy (no full anonymity [BMW04])
Signature Based Revocation (Sig-RL)
  In addition to basic signature, each signature also contains:
    B  G3 (B can be fixed if user wants linkability)
    K = Bf ( f :: Private Key)
    <B,K> added to signature in addition to <A, x, y>
  Sig-RL consists of [<B1,K1>, <B2,K2>, …, <Bn,Kn>]
  Signing a message requires proving in ZK that (K = Bf  Kj  Bjf) [CS03]
Not Verifier Local Revocation [BS04]
  Signer needs a live copy of revocation list
  For same message m, and same signer S, the signature length can different

## Slide 14: SGX EPID Provisioning (1)

## Slide 15: EPID Provisioning (2)

## Slide 16: EPID Quoting Enclave

## Slide 17: EPID Quote Verification Pitfalls