## Slide 1
Yogesh Prem Swami
SGX Remote Attestation is not sufficient

## Slide 2: Roadmap
Pitfalls in Protocol Composition
  Sequential Composition
  Concurrent Composition
  Enclave State Malleability
EPID Provisioning and Remote Attestation
  EPID Signatures
  SGX EPID Key Provisioning
  SGX Quoting Enclaves

## Slide 3: HW/SW crypto co-design
How to ensure that remote endpoint is a real hardware
Class-1 Simulation
  Run simulator on general hardware
  Countermeasure: Oracle access to a hardware resident key
Cass-2 Simulation
  Run simulator inside real hardware to man-in-the-middle
  Countermeasure: More difficult
SGX protects against both Class-1 and Class-2 Simulator
Class-1 Simulator
enclave
SGX
enclave
SGX Simulator
attacker
Class-2 Simulator
enclave
SGX
enclave
SGX Simulator
attacker
SGX

## Slide 4: Common SGX Enclave Design
STEP-1: Define a generic Remote Attestation Scheme
STEP-2: Arbitrarily compose different cryptographic schemes
  Generate keys, save them to disk
  Generate CSR requests
  Create Audit Log etc.
STEP-3: Define a workflow that combines STEP-1 and STEP-2 to achieve the goal
Several examples (both published as well as propriety)
Is this design paradigm secure?

## Slide 5: Sequential Composition
Example vacuously broken
  Attacker runs attestation correctly
  Runs rest of the protocol outside the enclave
Allows attacker to simulate some sub-computations
  commitment log of confidential data (e.g., sha256 of someone’s birthdate)
  Send confidential data (birthdate) encrypted over TLS
  Simulate states related to birthdate
Enclave is a single protocol sequentially composed of sub-protocols
Simulate

## Slide 6: Concurrent Composition

## Slide 7: Concurrent Composition
Attacker runs the same enclave concurrently
  Feed the same <tpm_cntr,tpm_sig> to both instances
Concurrent composition not limited to running same operation
SGX Has no in-built replay protection
  Adding TPM to TCB non-trivial
Launch Enclave cannot limit concurrency
  EINITTOKEN is a long-term credential
  Whitelist ineffective

## Slide 8: State Malleability and Knowledge Extractors
SGX enclave is not a black-box
  Adversary can force the enclave to exit at arbitrary execution point via AEX
  Adversary controls what happens after AEX
Global enclave state is malleable
Partial rewinding effect possible
  SGX allows multiple threads within the same enclave
  Interrupt one-thread at appropriate point
  ecall other threads
Careful with interactive Proof-of-Knowledge (PoK) protocols
  -protocols require just 2 response per commitment to reveal the secret
cntr = 0
cntr+1
cntr-1
cntr + n

## Slide 9: SGX EPID Provisioning and Remote Attestation

## Slide 10: Motivation
How to prove that Hardware knows a secret
  Use signature-of-knowledge scheme (e.g., Schnorr signature)
  Concerns about user privacy
SGX Solution
  Use group signatures

## Slide 11: Group Signature Overview
Members can anonymously sign messages on behalf of the group
  Single group public-key
  Unique private-key per-member
Group manager decides who joins the group
  Grants membership credentials to each member
Several security goals
  Fully Anonymity [BMW03]
  Member revocation [BL09]
EPID [BL09]:
  Anonymity
  Blinded join
  Member revocation

## Slide 12: Enhanced Privacy ID (EPID)
Two distinct components
  Basic Signature
  Non-revoked signature proof
Basic Signature based on BBS+ [BBS03, ASM06]
  q-SDH assumption
  CCA2 Secure in standard model
EPID construction
  Join: BBS+ signature on member’s private-key () in ZK
  Sign: Proves knowledge of BBS+ signature in ZK
Blinded join process
  No concurrent join
BBS+ Signature Scheme

## Slide 13: EPID Revocation
In addition to basic signature, each signature also contains:
  B  G3 (B can be fixed if user wants link-ability)
  K = Bf ( f :: Private Key)
  <B,K> added to signature in addition to Basic Signature
  In SGX B = EcHash(SPID || <randomdata>)
Signature Based Revocation (Sig-RL)
  Sig-RL consists of [<B1,K1>, <B2,K2>, …, <Bn,Kn>]
  Signing a message requires proving in ZK that (K = Bf  Kj  Bjf) [CS03]
Private-Key Based Revocation (Priv-RL)
  Member’s private-key directly placed in the revocation list
  Retroactively destroys member’s anonymity (no full anonymity [BMW04])

## Slide 14: SGX Remote Attestation Big Picture
EPID Provisioning
  How to join an SGX EPID Group
  Handled by PvE and PcE Intel Signed enclaves
  Uses Root Provisioning Key as Root of Trust for joining the Group
Remote Attestation
  Generate EPID Signatures on enclave’s identity (mrenclave, mrsigner, attr)
  Handled by QE (Quoting Enclave)
YES/NO
enc(epid_sig)
EPID Blinded Join and
PoK of RoT
SGX CPU
RoT established
at mfg.
EPID Key Gen
Group Membership Credentials
IAS
QE
enclave
local_attest(qe), nonce
enc(epid_sig), local_attest(enclave)

## Slide 15: SGX EPID Provisioning

## Slide 16: SGX EPID Provisioning
Each platform given a Provisioning ID (PPID)
  ppid  cmac(provision_key, 0128)
  Platform provisioning is not anonymous
EpidJoin (PvE/PcE action)
  ECDSA signature to convince IAS about hardware resident key
  Encrypts EpidJoinRequest with Provisioning Key
  Encrypts and uploads member’s private-key using Provisioning Seal Key
End result
  Group Membership credentials
  SGX EPID Group ID

## Slide 17: Remote Attestation
Service Provider (SP) and IAS establish
  SP Certificate + Service Provider ID (SPID)
Enclave creates local attestation for QE
  Optionally request QE to generate local attestation on Quote for Enclave
QE Creates encrypted EPID Signature
  Enclave validates QE’s local attestation on encrypted Quote
Enclave sends Encrypted Quote to SP
  SP cannot validate the quote itself even if it has access to Group Public Key
SP get Quote Validity YES/NO from IAS
local_attest,
SPID, nonce
IAS
SP
Enclave
QE
Cert
SPID
enc(epid_sig),
local_attest
enc(epid_sig)
enc(epid_sig)
Yes/No

## Slide 18: Conclusion
Provisioning Enclave and Quoting Enclaves are securely implemented
  But lots of bike shedding crypto
  Secure against sequential, concurrent, and state malleability
No privacy in-spite of group signatures
  Provisioning uses PPID to identify platforms
  Remote attestation quotes are encrypted and can only be validated by Intel
    Destroys privacy
    Could be abused for MitM

## Slide 19
Questions?

## Slide 20
Backup Slides

## Slide 21: SGX Key Hierarchy
Two statistically independent base keys
Root Provisioning Key
  Known to Intel
  Used during EPID Join
Root Seal Key
  Intel claims not to know this
  Unclear if key is generation via oracle access or injected from outside
Several named-keys derived from base key
  Coarse Access Control by Launch Enclave

## Slide 22: SGX Key Derivation
Each named key can further be diversified
  Enclave’s own identity (mrenclave, mrsigner, attributes)
  Potentially adversarial selected 128-bit random number
Identity used directly from CPU’s private data structures
  Absence  Use zeros
Keys cannot be diversified for other enclave’s identity

## Slide 23: SGX Local Attestation
Allows source enclave to prove that it’s identity is valid to any target enclave
  Allows 512-bits additional report data
EREPORT provides oracle access to target enclave’s ReportKey
  cmac over source enclave’s identity present in CPU (cannot be forged)
  Randomized by CR_REPORT_KEYID set at bootup time
Target enclave manually computes the CMAC using it’s own ReportKey