## Slide 1
Yogesh Prem Swami
Secure Substrates

## Slide 2: HW/SW crypto co-design
Software Simulation of HW as attack vector
Class-1 Simulation
  Simulate HW on any UTM
  Counter measure: Oracle access to a hardware resident key
Cass-2 Simulation
  Run simulator inside real hardware
  Simulator gets (oracle) access to keys
  Counter measure: More difficult
Intel SGX secure against both!
Class-1 Simulator
enclave
SGX
enclave
SGX Simulator
attacker
Class-2 Simulator
enclave
SGX
enclave
SGX Simulator
attacker
SGX

## Slide 3: Common SGX Enclave Design
STEP-1: Define a generic Remote Attestation Scheme
STEP-2: Arbitrarily compose different cryptographic schemes
  Load encrypted Private Key from Disk into Enclave
  Load authenticated Public Keys from Disk into Enclave
  Create signed/mac-ed Audit Log of events (e.g., which key was used, etc.)
  Make arbitrary ecalls, ocalls, and exit from enclave due to interrupts
STEP-3: Define a workflow that combines STEP-1 and STEP-2 to achieve the goal
Several examples (both published as well as propriety)
Is this design paradigm secure?

## Slide 4: Sequential Composition
Example vacuously broken
  Attacker runs attestation correctly
  Runs rest of the protocol outside the enclave
If |1| > 2x and the |2| > 2y then
  1 2 ≠ 2 1
  |i j | ≱ 2min{x,y}
  E.g., Mac-and-Encrypt vs. Encrypt-then-Mac
Sequential composition of protocols not always secure
  Enclave is a single protocol
  Broken mean bounds of the enclave protocol within known cryptanalysis limits

## Slide 5: Concurrent Composition
Attacker runs the same enclave concurrently
  Feed the same <tpm_cntr,tpm_sig> to both instances
Attacker runs different enclaves with same mrsigner in parallel
SGX Has no in-built replay protection
  Adding TPM to TCB non-trivial
  TPM and CPU needs mutual auth (motherboard/CPU swap!)
Launch Enclave cannot limit concurrency
  EINITTOKEN is a long-term credential
  Whitelist ineffective

## Slide 6: SGX Computational Model
SGX enclave is not a black-box (Oracle)
  Adversary can force the enclave to exit at arbitrary execution point via AEX
  SGX allows making ecalls after retuning from interrupts
SGX allows multiple threads within the same enclave
  Select number of allowed threads carefully!
Makes global state in enclave malleable
Requires careful ecall interface for Proof-of-Knowledge (PoK) protocols

## Slide 7: State Malleability and PoK extractor
/* count of generals who have authorized launch. */ static int auth_count = 0;
/* hardcoded list of generals and their PKs */ struct general_info{ char general_name[256]; const sgx_ec256_public_t general_pub; bool has_authorized; // initialized to false }GENERALS[] = { ... };
/* ecall made by each general with a sig on name + aux data */ int auth_and_launch(const char* const general_name, const sgx_ec256_signature_t* sig){ struct general_info* valid_general = validate_general(general_name, sig);
if(!valid_general){ return INVALID_GENERAL; }
if(!valid_general->has_authorized){ auth_count++; // AES here will be devastating! valid_general->has_authorized = true; }else{ return GENERAL_ALREADY_AUTHORIZED_ACTION;/* replay*/}
if(auth_count == 2){ return nuke_the_kashbah(location); }
return PENDING_AUTHORIZATION; }
Attacker runs the same enclave in parallel
  poly(instr-count)
Randomly interrupt the CPU
Make ecall with same input parameter
With multiple threads, one might be able to exploit PoK protocols

## Slide 8: SGX Remote Attestation

## Slide 9: SGX Key Hierarchy

## Slide 10: SGX Key Derivation

## Slide 11: Remote Attestation Overview (1)

## Slide 12: Remote Attestation Overview (2)

## Slide 13: Enhanced Privacy ID (EPID)

## Slide 14: EPID Revocation

## Slide 15: EPID Provisioning (1)

## Slide 16: EPID Provisioning (2)

## Slide 17: EPID Quoting Enclave

## Slide 18: EPID Quote Verification Pitfalls